Developing Film

1 roll = 300 mL/11 oz				2 rolls = 600 mL/22 oz

- Load film into developing tanks after rolling your film

- Get chemicals ready (WEAR GLOVES, check developer temperature = 70()

- Pre-wet: 1 minute - Agitate for 1 minute to remove coating from film and to prevent discoloring (SET TIMER)

- D-76 Developer: 12 minutes total (stock mix = mix with water 1:1 = 5.5 oz developer and 5.5 oz of water) (70(F)

  - Agitate 30 seconds

  - Rest 1 minute

  - Agitate for 5 seconds every minute

  - Rest 1 minute…..until 12 minutes is up

  - Dump out chemical and run water down drain

- Stop Bath: (working solution =  no mixing needed)

  - 30 seconds full agitate

  - SAVE STOP when done…Do Not pour down drain

- Fix: 5 minutes total (working solution mix = no mixing needed)

  - Agitate for 5 seconds

  - Rest 1 minute

  - Agitate for 5 seconds every minute…until 5 minutes is up

  - SAVE FIX in used container

- Water: Wash with water for 5 minutes (Let water run on top & dump out every minute)

- Photo Flo solution: agitate for a few seconds

- Squeegee with finger and hang dry